## Slide 1
Karel Kubíček
F5351
Proteiny II – studium proteinů při atomárním rozlišení
Přednáška je podporována grantovými prostředky z programu:

## Slide 2
15NH4Cl, 37oC
13C-glukosa
supernatant odstraníme odstředěním
ultra-centrifugace

## Slide 3
NMR - refresh
nuclear spin  0 (1H, 13C, 15N, 31P)
- number of neutrons and the number of protons both even  NO nuclear spin - number of neutrons plus the number of protons odd  half-integer spin (i.e. ½, 3/2, 5/2) - number of neutrons and the number of protons both odd  integer spin (i.e. 1, 2, 3)
=*B (1) - when placed in a magnetic field of strength B, a nuclei with a net spin can absorb a photon, of frequency . The frequency  depends on the gyromagnetic ratio,  of the nuclei
from quantum mechanics we know that nucleus with spin I can have 2I +1 orientations  nuclei with a spin ½ can have two orientations in an external magnetic field– low / high energy
N
S
N
S
N
S
E=h  (2)

## Slide 4
Magnet
superconductive solenoids on the basis of
Nb and Sn immersed in helium bath
He-bath ~4 K further cooled with J-T
pump up to ~2.1 K
- nowadays spectrometers ~ 22 Tesla
(Nb, Ta)3Sn superconductive wire 0.81 mm in diameter with 271 filaments buried in OFHC copper matrices

## Slide 5
bore cca 55mm
He-fill
N2-fill

## Slide 6
NMR spektrometr
Magnetické pole země
~ 50mT

## Slide 7
NMR probehead

## Slide 8
Spectrometer
CBU
Control board unit
FGU
Frequency gen. u.
Shimms
Temperature Unit
AcquisitionControler
Transmitter

## Slide 10
Resonance condition w0 = -gB0

## Slide 12
Zlepšení citlivosti, rozlišení a intenzity NMR magnetů
J. Emsley &
R. Feeney,
Progr.. NMR
Spectroscopy 1995, 28, 1
‘10
1945
60
1961
220
1965
1973
360
1979
500
1987
600
1992
750
1000
‘97
2000
‘68
decoupling
decoupling
TROSY
FT and nD
DNP in high
fields
Spectrometer Frequency [MHz]
Time [year]

## Slide 13
MHz | T(esla)
200 | 4,6975
250 | 5,8719
300 | 7,0463
400 | 9,3950
500 | 11,7440
600 | 14,0926
700 | 16,4416
750 | 17,6157
800 | 18,7900
1H NMR frekvence v daném mg. poli

## Slide 14
(Y1S2P3T4S5P6S7)n
RNA Pol II
P
P
P
RNA Pol II CTD recruits processing factors
Notes: RNA Polymerase II recruits various co-transcriptional processing factors via its C-terminal domain. Recruitment of processing factors at different stages of the transcriptional cycle is controlled by a specific phosphorylation at Serines two five and seven or their combinations that create a so called - CTD code that is not fully understood yet.

## Slide 15
CTD of RNA polymerase II
Adapted from Mol. Cell 36:541-6, 2009
Nature 430: 223-6, 2004
Mol.Cell 11: 1549-61, 2003
Notes: number of structural works suggested how CTD code could work. First, NMR studies of nonphosphorylated CTD suggested that the free CTD is largely flexible with some residual structure and a tendency to form SPXX beta-turns Occurrence of the beta-turns affects whether the entire CTD forms either extended, loose spiral or compact beta-spiral structure.
The X-ray structures of Pcf11 bound to Ser2-phosphorylated CTD and Cgt1 bound to Ser5-phosphorylated CTD, show that the conformation of the bound CTD is templated by their binding partners.
While Pcf11 induces a beta-turn conformation of the CTD that is stabilized by additional H-bond involving phosphogroup of the serine 2.
The Cgt1 induces an extended conformation of the CTD and the interaction is based on contacting phospho groups and large hydrophobic interactions.

## Slide 16: Nrd1-dependent termination mediated by Nrd1/Ess1/Ssu72
Adapted from Mol. Cell 36:255-66, 2009
Ssu72
Notes: This most flexible Ser 5 phosphorylated CTD is involved in recruitment of proteins involved in the Nrd1-termination pathway that operates for many non-coding RNAs. Although it is not clear how this termination mechanism operates, three proteins seem to be critical in this mechanism. Nrd1 that binds the Ser5P-CTD, Ess1 cis/trans isomerase that is involved in the dissociation of CTD from Nrd1, and Ssu72 phophatase that removes the phosphate from the serine. However, how this works structurally and mechanistically is not known. Hence, our aim is to get the structural and mechanistic view on this process.

## Slide 17: Interaction of Nrd1-CID with C-terminal domain (CTD)
(Y1S2P3T4S5P6S7)
P
CTD
RRM: RNA recognition motif; CID: CTD interaction domain; CTD: C-terminal domain
CID
RRM
RNA Pol II
Nrd1
RRM
RRM
CID
154
575
1
Nrd1
Notes: System, that will be further discussed in this talk is composed of Nrd1-CTD interaction domain that is about 150 amino acids long and CTD will be represented by two heptad repeats phosphorylated at serine 5.

## Slide 18
15N-1H HSQC
1 peak ≅ 1 amino acid
Excelent info about the protein fold
No info about primary sequence

## Slide 19: Interaction of Nrd1-CID with C-terminal domain (CTD) NMR Titration - 15N enriched CID + unlabeled CTD-Ser5P in n-steps, n=6 in our case - peaks corresponding to the interacting residues of CID change their chemical shift (position in the spectrum) => interaction surface, binding constant, stoichiometry
Notes: We studied the interaction between CTD and CID by monitoring the chemical shift changes of the CID residues – one peak represents one amino acid in this spectra - upon addition of the CTD. In this way, we indentified the interacting surface of the Nrd1-CID

## Slide 20: Interaction of 15N enriched CID with unlabeled CTD-Ser5P in n-steps, n=6 in our case - peaks corresponding to the interacting residues of CID change their chemical shift (position in the spectrum) =>interaction surface, binding constant, stoichiometry
Notes: Monitoring the chemical shift prerturbations of the Nrd1-CTD interacting domain upon addition of the CTD we wanted to know how Nrd1-CID associate with Ser5P-CTD. In this way, we indentified the interacting surface of the Nrd1-CID

## Slide 21: Nrd1 CID interaction surface –
Notes: With the knowledge of the NMR three dimensional structure of the CID and the residues pertubed upon complexation with Ser5P-CTD, we can identify the CTD-interacting surface, that consists of these residues......

## Slide 22: Nrd1 CID interaction surface – CID residues experiencing the largest chemical shift variations upon the interaction with 5-phospho-Ser CTD shown in blue with side-chains in stick representation
Notes: … that are located on three helices of the CID.

## Slide 23
CTD-CID interaction with mutants studied by fluorescence anisotropy
Notes: Additionally, still analyzing the chemical shift perturbations, we have selected the residues crucial for the interaction and have mutated them to observe a dramatic drop in the affinity as measured by fluorescence anisotropy.

## Slide 24
Interligand NOEs between CID and CTD – 900MHz, 150ms, 293K
CID resonances
CTD resonances
Notes: Next, we determined the NMR structure of the complex between Nrd1-CID and Ser5P-CTD by measuring intermolecular contacts that are defined by these NOEs, where in one frequency domain, we acquired the resonances of the protein and in the second dimension the resonances of the ligand.

## Slide 25
X-ray Pcf11 NMR-derived Nrd1-CID
Pcf11 + P1S2Y3pS4P5T6S7P8S9 Nrd1-CID +
Y1S2P3T4pS5P6S7Y8S9P10T11pS12P13S14
– 1 CTD repeat unit
Notes: With the help of intermolecular NOEs we obtained structure of Nrd1-CID bound to Ser5P-CTD, in this slide compared with Pcf11 on the left. The peptide is in extended conformation. It partly resembles the structure of Pcf11 bound to Ser2P-CTD. However, there are few important differences. In the Nrd1 structure, the pS5-P6 bond is in the cis conformation. This conformation enhances the hydrophobic contacts between the peptide and Nrd1. Also, phosphate group of Serine 5 might contact R74 of Nrd1 as they are in close proximity in the cis conformation but we do not have a direct experimental evidence for this as phosphate group is difficult for NMR spectroscopy.

## Slide 26
NMR measurement of Ess1 prolyl isomerase
unique substrate specificity:
pSer-Pro or pThr-Pro
containing peptides
CTD + Ess1 prolyl isomerase
Y1S2T3P4-pS5-P6-S7Y8S9P10T11-pS12-P13-S14
2D projection of a 3D 13C-NOESY
of (YSPTpSPS)2
in absence
and presence of Ess1
trans
cis
Free energy
Transition state
DG#tc
DG#ct
DGeq
DG#cat
+PPIase
Adapted from Nat Chem Biol 3:619-29, 2007
DG#tc > DG#ct
trans to cis rare
DG#ct ≈14-24kcal/mol
180°
Hd-cis/trans
Hd-trans/cis
Ha-trans/cis
Ha-cis/trans
Notes: Second important player in this mechanism is the Ess1cis/trans prolyl isomerase. It has been shown that Ess1 binds CTD phosphorylated at position two or five but it does not bind unphosphorylated CTD and that catalytic activity of this enzyme is important for the proper termination.
First, from our NMR data we can confirm conformation exchange between cis and trans forms.

## Slide 27: 1H15N Chemical shift changes of CID upon titration by pSer5 CTD and subsequently Ess1
CID CTD
CID CTD + Ess1 1st addition
CID CTD + Ess1 2nd addition
CID-CTD complex + ESS1 isomerase
Free
CID
CID
+CTD
1st+2nd add Ess1
Notes: And secondly, when we studied the role of Ess1, we observed that upon a two step addition of the Ess1 to the CID-CTD complex, some of the residues that upon formation of the CTD-CID complex moved towards bound position were shifting back to the free form of the CID protein, as you can see from diminishing chemical shift perturbations of the CID residues.

## Slide 28
Ess1 mediated dissociation mechanism
Notes: Here you can see the CID-surface colored blue for residues that are affected upon CID-CTD complex formation and some of these are returning back upon Ess1 addition suggesting that CTD is not in contact with them any longer.
Based on our NMR data, we propose the following mechanistic model. Ess1 converts Pro6 from cis to trans conformation and thus promotes the dissociation of CTD from the Nrd-CID binding surface.

## Slide 29
…S5cisP6…
P
cis-trans isomerization in the “CTD code”: CTDpSer5-Proline isomerization in the CTD controls binding and dissociation of Nrd1-CID
…S5transP6…
P
Nrd1-CID binding
ESS1 isomerase
Ssu72 phosphatase
…S5transP6…
Notes: In summary, we suggest that the specific binding of CTD is not only encoded in the site specific phosphorylation but also in the non-covalent changes in the CTD structure, such as prolyl isomerization. In such model that is relevant to the Nrd1 termination pathway, Nrd1 preferentially binds the cis conformation of phoshpoSer-Pro bond. when Ess1 comes into the play, it changes the cis-to-trans conformation and thus promotes the dissociation of CTD from Nrd1. The trans isomer of pSer-Pro is then the target substrate for the Ssu72 phosphatase that dephosphorylates phosphoserine 5. This concerted isomerization and dephosphorylation events are important for the correct termination for many non-functional RNAs. Additional info poster #113.

## Slide 32
SAXS/EXAFS
EXAFS poskytuje informace o nejbližších slupkách atomů sousedícíh s absorbujícím atomem
Fe
N
N
N
N

## Slide 33
His 108
Met 75
Met 86
Met 110
Cu(I)
b4
b5’
X-Ray Absorption Spectroscopy
Cu(I)DR1885 DE=-10.3 eV
Ligand r(Å) 2s2.103(Å2) R-exafs e(fit index)
Fit1 (1shell) 2S 2.299 4(1) 0.446 0.49
Fit2 (1shell) 3S 2.301 9(1) 0.403 0.41
Fit3 (2shells) 3S 2.300 8(1) 0.334 0.29
1N§ 1.982 4(1)
Fit4 (2shells) 3S 2.303 8(1) 0.305 0.27
1N* 1.999 7(2)
§ no MS *His, MS

## Slide 35
Peptide Mapping with MALDI TOF
Tryptic digestion o/n 1:30-50 (trypsin:protein)
Analysis with PAWS (Genomic Solutions, Inc.)
Apo
Cu1+
Cu2+

## Slide 36
Motivation

## Slide 37
Terminology
X-ray – diffraction / scattering
XS - X-ray scattering
SAXS/WAXS - Small/Wide Angle X-ray Scattering
SANS - --------”---------- Neutron ---”---
Otto Kratky (1902, Vienna-1995, Graz)
Günter Porod (1919 near Villach, 1984 Graz)
Dmitri I. Svergun
Scattering
Scattering curve
Guinier plot
PDF (Pair-distribution function)
Bead model
Bead model - / SAXS - envelope

## Slide 38
Experimental setup
SAXS
X-ray

## Slide 39
SAXS
X-ray
Crystalized Sample Sample in Solution

## Slide 40
(very tiny) bit of theory
q=2k.sinq => q/2/k=sinq,
k=2p/l => q=4p/l.sinq
Often q is denoted as s
k
q

## Slide 41
=>
1st step: scattering to scattering curve

## Slide 42
What can we learn from the scattering curve:
Shape of the studied molecule
Fold
Secondary structure

## Slide 43
Is it really that easy?

## Slide 44
2nd step: Guinier plot (from the initial region of the scattering curve)

## Slide 46
3rd step: PDF Pair-distribution function

## Slide 48
All information from the scattering curve together

## Slide 49
Bead model
Spherical harmonics problem to be solved

## Slide 50
Solutions with similar “goodness” of fit may be obtained

## Slide 51
Summary

## Slide 52
Summary (graphically)

## Slide 59
Evaluation of the experimental data

## Slide 60
Challenge to be resolved

## Slide 61
References:
Koch, M.H.J., Vachette, P., Svergun, D.I. Quart Rev Biophys 2003
Jacques, D.A., Trewhella, J. Prot Sci 2010
Svergun, D.I., Petoukhov, M.V., Koch, M.H.J. Biophys J 2001
Wriggers, W. Biophys Rev 2010
Putnam, C.D., Hammel, M., Hura, G.L., Tainer, J.A. Quart Rev Biophys 2007
Madl, T. Gabel, F., Sattler, M. J Struct Biol 2010