## Slide 1
Karel Kubíček
F9600
Spektroskopické studium biopolymerů
Přednáška je podporována grantovými prostředky z programu:

## Slide 2: Analytical Ultracentrifugation

## Slide 3: Analytical Ultracentrifugation – Applications
determine sample purity
characterize assembly and disassembly mechanisms of biomolecular complexes
determine subunit stoichiometries
detect and characterize macromolecular conformational changes
measure equilibrium constants and thermodynamic parameters for self- and hetero-associating systems  characterize the solution-state behavior of macromolecules under various conditions

## Slide 4: Analytical Ultracentrifugation – Applications
determine sample purity
characterize assembly and disassembly mechanisms of biomolecular complexes
determine subunit stoichiometries
detect and characterize macromolecular conformational changes
measure equilibrium constants and thermodynamic parameters for self- and hetero-associating systems  thermodynamic and hydrodynamic information

## Slide 5: Analytical Ultracentrifugation – Design
analytical ultracentrifuge = preparative ultracentrifuge + optical detection system  measure sample concentration inside the centrifuge cell during or after sedimentation
centrifugation parameters and data acquisition under computer control  experiments lasting many days performed with minimal operator intervention

## Slide 11: Analytical Ultracentrifugation – Design: Optical systems
Absorbance optical system:  measurement of sample concentration at wavelengths from 200 to 800 nm  detection of macromolecules containing strong chromophores
Rayleigh interference optical system:  measurement of sample concentration based on refractive index changes  analyze macromolecules lacking intense chromophores (eg, polysaccharides) and samples that contain strongly absorbing buffer components (eg, ATP/GTP, DTToxidized)

## Slide 13: Analytical Ultracentrifugation – Sedimentation velocity experiments
Meniscus of solvent
Sedimentation front
Meniscus of solution
Plateau conc.
Cell radius
Concentration of solute
Modified from http://www.kolloidanalytik.de/uz/sed/uzsedhr.gif

## Slide 14: Analytical Ultracentrifugation – Sedimentation velocity experiments
Svedberg equation:
 influenced by density and viscosity of solvent  standard solvent (water, 20°C): s20,w
Boundary spreading: Flux J

## Slide 15: Analytical Ultracentrifugation – Sedimentation velocity experiments
Hydrodynamic information
Experimentally determined parameters:
  Sedimentation coefficient s
  Diffusion constant D or friction factor f
  Molecular mass M
  Estimation of the molecule’s shape in solution
High rotor speeds  sedimentation dominates diffusion

## Slide 16: Analytical Ultracentrifugation – Data analyses: sedimentation velocity
plot natural logarithm of boundary midpoint versus time  single-point boundary analyses  slope of straight line yields sedimentation coefficient s
time derivative (DCDT) method (Stafford)  subtract different scans  convert the boundaries into apparent differential distribution of s, g(s*) and plot g(s*) versus s*

## Slide 17: Analytical Ultracentrifugation – Sedimentation equilibrium experiments
Cell radius
Intensity
Diffusion
Sedimentation
Slower rotor speeds  balance between sedimentation and diffusion forces  no net transport  no influence of shape factors
Determination of M:
http://www.kolloidanalytik.de/uz/equil/hequil.pdf

## Slide 18
Sedimentation velocity is a hydrodynamic technique and is sensitive to the mass and shape of the macromolecular species. In a sedimentation velocity experiment, a moving boundary is formed on application of a strong centrifugal field. A series of scans (ie, measurements of sample concentration, c, as a function of radial distance, r) are recorded at regular intervals to determine the rate of movement and broadening of the boundary as a function of time.
In contrast, sedimentation equilibrium is a thermodynamic technique that is sensitive to the mass but not the shape of the macromolecular species. These experiments are performed at lower speeds and measure the equilibrium concentration distribution of macromolecules that eventually forms when sedimentation is balanced by diffusion.
The sedimentation velocity and equilibrium measurements provide complementary information, and it is often useful to apply both techniques to a given problem.

## Slide 19: Analytical Ultracentrifugation – Examples of Applications
Sedimentation velocity
  Biomolecular Shape
  Biomolecular Conformational Changes
  Assembly and Disassembly of Biomolecular Complexes
  Molecular Mass and Subunit Stoichiometry
  Equilibrium Constants for Self-Associating Systems
Sedimentation equilibrium
  Molecular Mass and Subunit Stoichiometry
  Equilibrium Constants for Hetero-associating Systems
  Equilibrium Constants for Self-Associating System

## Slide 21
f/f0 = 2.141890
meniscus 6.0495, bottom 7.2080 (fixed)
fitování 6.0654-7.1301
s* = 3.28 S S020,w = 3.62 S (Sednterp: f/f0 = 2.20) … dimer
s* = 4.82 S S020,w = 5.37 S (Sednterp: f/f0 = 2.35) … tetramer
cell 2: GST E2 26 his, 0.07 mg/ml
All the scans used for data analysis. Removing of TI noise, continuous c(S) distribution from 0 S to 50 S, confidence level of regularization 0.95.
3.28 S
loading concentration [signal] = 0.535905 (73.88% of total)
std deviation [as sqrt (second central moment)] = 0.092
MW= 93.7 kDa(gross estimate!!!)
4.82 S
MW= 192 kDa(gross estimate!!!)

## Slide 22
f/f0 = 2.141890
meniscus 6.0495, bottom 7.2080 (fixed)
fitování 6.0654-7.1301
s* = 3.28 S S020,w = 3.62 S (Sednterp: f/f0 = 2.20) … dimer
s* = 4.82 S S020,w = 5.37 S (Sednterp: f/f0 = 2.35) … tetramer
cell 2: GST E2 26 his, 0.07 mg/ml
All the scans used for data analysis. Removing of TI noise, continuous c(S) distribution from 0 S to 50 S, confidence level of regularization 0.95.

## Slide 23
3.25 S
loading concentration [signal] = 0.860558 (72.78% of total)
std deviation [as sqrt (second central moment)] = 0.085
MW= 108 kDa(gross estimate!!!)
4.75 S
MW= 208 kDa(gross estimate!!!)
f/f0 = 2.147410
meniscus 6.0486, bottom 7.2040 (fixed)
fitování 6.0674-7.1212
s* = 3.25 S S020,w = 3.63 S (Sednterp: f/f0 = 2.20) … dimer
s* = 4.75 S S020,w = 5.30 S (Sednterp: f/f0 = 2.38) … tetramer
cell 3: GST E2 26 his, 0.36 mg/ml